Report on the
Earth Rover Waypoint Navigation

EARTH ROVER

Date: March 30, 2018	Version: 0.1
Author:	Jonathan Cacace

# Introduction
The aim of this document is to support developers to properly configure and launch the programs to start the waypoint navigation with Earth Rover steering robot.
In the actual version of the navigation system, IMU and GPS sensors are used to drivre the robot during the navigation. The system can be used in Gazebo simulation as well.
In this documentation, is assumed that you are able to start the low-level hardware controller of the robot, instantiating the four wheels steering controller of the Earth Rover robot.
To start the navigation, we need to launch the following ROS nodes/packages:
- Imu sensor package
- Gps sensor package
- Earth Steering controller
- Earth Rover Localization
- Earth Rover Planner
- Eart Rover Navigation.
In the following the aim of the main packages/software involved in the navigation are discussed. While in the last section will be shown how to launch all the packages.
# Earth Steering

The earth-steering module is part of the earth-rover-ros repository. The main aim of this package in the navigation process is to translate the commanded linear and angular velocity generated by the move_base package in the four wheel steering controller message.
The mapping between these two messages is made by the base2steering executable, place in the src folder.
Input:
    /cmd_vel: [geometry_msgs/Twist], specifies the linear and angular velocity to move the base
Output:
   /four_wheel_steering_controller/cmd_four_wheel_steering:
        [four_wheel_steering_msgs::FourWheelSteering]: specifies the velocity for the fron and rear wheel and the steering
Parameters:
In the launch file placed in the ~/earth_steering/launch folder, you can specify the following parameters:
- max_x_vel: Maximum linear velocity
- delta_max: Maximum angular steering
- wheelbase: The length of the robot base

Launch this node:
      $ roslaunch earth_steering earth_steering.launch

Possible improvements:
- Made a more precise mapping between the base linear and angular velocities could increase the performance of rover navigation
- The input /cmd_vel topic could be split to take into account autonomous or manual velocity commands
# Earth Rover Localization
# The earth rover localization is needed to localize the robot a local cartesian coordinate frame. Currently it uses IMU and GPS but could be estened to other odometry source in the future. The localization uses the robot_localization package (http://docs.ros.org/api/robot_localization/html/index.html), running the following node:
# navsat_transform_node: navsat_transform_node takes as input a sensor_msgs/Imu containing an accurate estimate of your robot’s heading, and a sensor_msgs/NavSatFix message containing GPS data. It produces an odometry message in coordinates that are consistent with your robot’s world frame. This value can be directly fused into your state estimate.
# ekf_localization_node: Implements an extended kalman filter, taking as input the output of the navsat_transform_node and the IMU.
# To set the parameters of these nodes you shouold edit the launch file placed in ~/earth_rover/launch/earth_rover_localization.launch file. In particular:
# navsat_transform_node: <remap from="imu/data" to= YOUR_IMU_TOPIC /> <remap from="gps/fix" to=YOUR_GPS_TOPIC />
# ekf_localization_node: <param name="imu0" value=YOUR_IMU_TOPIC /> <param name="odom0" value="odometry/gps"/>
# You also need the Fixed transofmation between the Robot base_link and the sensors: Gps and Imu:
# …. TODO: add more inforomation here!
Launch this node:
      $ roslaunch earth_rover earth_rover_localization.launch
# Earth Rover Planner
# The earth_rover_planner is based on the teb_local_planner and move_base ROS packages. Given a Map (the crop field map for instance), the move_base package implements an action service to generate a geometric free path to reach robot destination. The teb_local_planner is then used to navigate this path in a local way, considering the dynamic of the robot and the new path obst
# teb_local_planner: The teb_local_planner package implements a plugin to the base_local_planner of the 2D navigation stack. The underlying method called Timed Elastic Band locally optimizes the robot's trajectory with respect to trajectory execution time, separation from obstacles and compliance with kinodynamic constraints at runtime.
# move_base: The move_base package provides an implementation of an action that, given a goal in the world, will attempt to reach it with a mobile base. The move_base node links together a global and local planner to accomplish its global navigation task
# After launched teb_local_planner and move_base, you could ask a new plan calling the move_base acion server (this is implemented in the earth_rover_navigation package).
# Configure thes nodes:
# After installed these nodes in the earth_rover_robot, some configuration files are needed. Currently these file are stored in the ~/earth_rover/map_cfg folder and are in charge to configure both the local and global planners: costmap_common_params.yaml, global_costmap_params.yaml, local_costmap_params.yaml, maze.png, maze.yaml, teb_local_planner_params.yaml.
Launch this node:
      $ roslaunch earth_rover earth_rover_planner.launch
Possible improvements:
Considering the motion of the real rover, the parameters in the configuration files should be tuned.
# Earth Rover Navigation
# The documentation for t he earth-rover-navigation package is reported on the github page:
# https://github.com/earthrover/earth_rover_navigation
# Test Earth Rover Navigation in Gazebo simulator:
# To test the waypoint navigation in Gazebo simulator you should launch the following applications:
# Simulator:
# We need to run the Gazebo simulator along with GPS and IMU sensors:
# $ cd ~/earth-rover-ros/script
# $ ./launch_sim_with_sensors.sh
# Earth Steering:
# We need to remap the /cmd_vel topic generated by the planner with the four wheels steering controller:
# $ roslaunch earth_steering eart_steering.launch
# Localization:
# We need to launch the localization packages using the simulation sensor data:
# $ roslaunch earth_rover earth_rover_localization_gazebo.launch
# Waypoint Navigation:
# Launch the waypoint navigation planner with the Rviz User Interface:
# $ roslaunch earth_rover earth_rover_planner_ui.launch
# Launch the waypoint navigation package
# $ rosrun earth_rover_navigation earth_rover_nav
# Add waypoints from file:
# $ rosrun earth_rover_navigation nav_client
# Start/pause/continue navigation using ROS services.
# Test Earth Rover Navigation in Real Robot:
# ...TODO...